## Slide 1: Research and create a diagram of how data is transmitted from a client to a server over the internet.

## Slide 2
In the client-server model, data transmission follows a structured journey across several layers of hardware and software protocols.
The Data Transmission Process
Request Initiation: The process begins when a user enters a URL or triggers an action in a client application (like a web browser).
DNS Lookup: The browser contacts a DNS (Domain Name System) server to translate the human-readable domain name (e.g., google.com) into a numerical IP address required for routing.
Packetization: The Transmission Control Protocol (TCP) breaks the data request into smaller units called packets. Each packet contains a sequence number and the IP addresses of both the sender and receiver.
Routing: Packets are sent from the client to an Internet Service Provider (ISP) and then through a series of routers and switches. These packets may take different physical paths across the internet's backbone of optical fiber cables to reach the destination.
Server Processing: Once the packets arrive at the server's IP address, the server reassembles them in the correct order. The server processes the HTTP/HTTPS request and sends back the requested data (such as HTML, images, or files) using the same packetized method.